## Slide 1
Introduction to ASYN Design, Features and Usage

## Slide 2: The ASYN Framework
Parts and concepts
Functional and data interfaces
ASYN processing: asynchronous and synchronous
Advantages
Tracing and debugging
Use cases

## Slide 3: ASYN Parts and Concepts
Generic EPICS Device Support for all record types
  No need to write Device Support
Pluggable named ports
  One thread per blocking port
  ASYN does thread handling, queueing, locking, protection
Named data type interfaces
  Drivers implement interfaces based on their data types
Interpose layers
  Allow building layered protocol stacks from reusable blocks
Tracing facility

## Slide 4: ASYN Port Interfaces
Functional
  Connection handling
  Status
  Tracing and error handling
Data
  Octet (stream of bytes)
  Int32, UInt32
  Float64
  Arrays: Int8, Int16, Int32, Float32, Float64
  Enum
  Opaque pointer

## Slide 5: ASYN Processing: Synchronous
Scanner thread
Blocking IO
PACT=0
Record Support
ASYN DevSup
ASYN
Callback
Lock port
Unlock port
Port Driver

## Slide 6: Record Processing: Synchronous
Scanner thread
PACT=0
Record Support
Device Support
Driver Support
Blocking IO

## Slide 7: ASYN Processing: Asynchronous
Callback thread
Port thread
Scanner thread
Record Support
ASYN DevSup
PACT=0
Leaving PACT=1
PACT=1
work queues
Blocking IO
Callback
Request processing
Lock
Unlock
Port Driver
ASYN

## Slide 8: Record Processing: Asynchronous
Callback thread
IRQ
Scanner thread
Record Support
Device Support
Driver Support
IO Request
PACT=0
Leaving PACT=1
PACT=1
IO Response
Request processing

## Slide 9: ASYN Advantages
Minimizes user code
ASYN handles all the complex parts:
  Device Support layer
  Thread handling
  Proper resource locking
  Queueing (by priority)
Ports Drivers can be stacked
  High level Port Driver for a device (data interfaces)
  Low level Port Driver for a connection (octet interface)

## Slide 10: Tracing and Debugging
ASYN trace facility enforces streamlined debug and error messages
asynRecord provides access to full ASYN capabilities for debugging (useful to have one of those on each IOC that uses ASYN)

## Slide 11: asynPortDriver C++ Base Class
Using the C API requires a lot of boilerplate:
  Creating handles
  Registering ports and interfaces
  Calling interrupt clients
  …
asynPortDriver takes care of all this
  Adds generic parameter get/set facility
Using this C++ base class is the recommended way to create a Port Driver

## Slide 12: Applications 1) Swapping a Driver
Instrument (vacuum pump) on a serial connection
Lab setup: serial line connected to IOC
Production setup: serial line to terminal server, IOC connects through TCP/IP
ASYN can at startup (or in the live system) switch the low level (octet) driver from drvAsynSerialPort to drvAsynIPPort, without changing the high level driver (for the pump) or the EPICS database

## Slide 13: Applications 2) Swapping a Protocol
Siemens PLC (with SPSS communication package) using the next version of S7Asyn driver
ASYN can at startup switch the high level (items in PLC data block) driver from Raw TCP block read/write to the Native S7 protocol, without changing the EPICS database.

## Slide 14: Applications 3) Adding a Checksum
Device offers same protocol on TCP/IP and RS232, but the RS232 needs checksums after each message.
An ASYN interpose module can implement the calculation/adding (on send) and check/removal (on receive) of a checksum.
Then the low level (octet) driver can again be switched from drvAsynSerialPort with checksum interpose to drvAsynIPPort, without changing anything above.

## Slide 15: Conclusion
ASYN extends the somewhat sloppy EPICS device interface
Device driver framework with pluggable reusable modules
Data type specific interfaces (instead of record type)
Interpose modules to implement protocol stacks
Tracing/debugging support
Convenience C++ base class
Questions?

## Slide 16: EPICS Device Interface
IOC architecture: EPICS support layers
Traditional Device and Driver Support APIs
Record processing: synchronous and asynchronous
Caveats

## Slide 17: IOC Architecture
APIs are
Well defined
Well defined
Pretty well defined
Poorly defined

## Slide 18: Device and Driver Support APIs
Device Support: jump table per record type
  report
  init (once per support)
  init (per record instance)
  rec type specific io (read or write)
  get interrupt info (if interrupt scan is supported)
  rec type specific calls (e.g. conversion factor update)
Driver Support: jump table
  report
  init
  …

## Slide 19: Classical Device/Driver Support
Needs to implement Device Support functions for all supported record types
  For a multi-purpose device easily ~10 record types
  Must understand how all these record types work
Uses private API between Device and Driver Support
  Device Support is strongly coupled to a Driver
  Making it practically impossible to swap the Driver (to use e.g. a different serial line IO board)
Each Device/Driver support has their own API, style and format for debugging/tracing

## Slide 20: Record Processing: Synchronous
Scanner thread
PACT=0
Record Support
Device Support
Driver Support
Blocking IO

## Slide 21: Record Processing: Asynchronous
Callback thread
IRQ
Scanner thread
Record Support
Device Support
Driver Support
IO Request
PACT=0
Leaving PACT=1
PACT=1
IO Response
Request processing

## Slide 22: Asynchronous Processing Caveats
Multi-threaded environment
  Often processing/waiting is offloaded to separate threads
  All access to shared data (record, buffers, queues) between threads must be properly guarded by semaphores
Record priorities
  Three priority levels, configured in record instance
  Device Support architecture should support this
  Actually: most Device Supports don’t

## Slide 23
Thank You for Your Attention!
Credits: