## Slide 1
Working with EPICS
-simple device integration-

## Slide 2
Task: integrate a simple power supply using StreamDevice
This demo/exercise will show you the “barebones” method of setting up an IOC.
  Don’t be too scared. It gives you an idea what is behind the scenes.
The community does not (yet) provide a common, universal setup tool.
  Several institutes have built their own environments to make this easier.
    For instance our (ESS) build and management tool, the e3.
  For this simple setup I decided to use the off-the-box method.
The site docs.epics-controls.org has a couple of “getting started” recipes.

## Slide 3
Task: integrate a simple power supply using StreamDevice
The simulated device is a variable voltage power supply unit controller, offering a simple interface and message-based protocol.
The device listens on TCP/IP port <check the code >.
It expects input commands following a known format followed by an End-Of-Line indicator.
To each known command, it returns a specific reply, also followed by an End-Of-Line indicator.
The End-Of-Line indicator in both directions is CR LF (CarriageReturn followed by LineFeed: \r\n). This is used to determine when a message ends and the next one begins.

## Slide 4
Task: integrate a simple power supply using StreamDevice
The following table displays the available commands the device simulator understands:
For a real-world reference, compare with a Lakeshore cryogenic controller (from Lakeshore-336 manual):

## Slide 5
Task: integrate a simple power supply using StreamDevice
Before starting the VM:
  In the “Extras” folder that you copied from the USB, there is a directory “streamIOC”. It contains a ready-made IOC for communicating with the simulated power supply. In the VM settings, map that directory to /mnt
Power up the VM. With the file manager, navigate to /mnt, and open a terminal there. (two or three windows or tabs will be needed.)
In one terminal window, start the simulator with:
  “python PSU.py”
  If you see a message reporting a port number, you are fine to go.

## Slide 6: Protocol File for the simulated power supply
# Stream protocol file for simulated PS
idn {
out "*IDN?";
in "%s";
}
power-rb {
out "POWER?";
in "%{OFF|ON}";
}
v-out {
out "VOUT?";
in "%f";
}
v-set-rb {
out "VSET?";
in "%f";
}
power-cm {
out "POWER %{OFF|ON}";
in "POWER SWITCHED %{OFF|ON}";
@init {power-rb;}
}
v-set-cm {
out "VSET %f";
in "VOLTAGE SET TO %f";
@init {v-set-rb;}
}
}

## Slide 7: Example record definitions from the database
record(stringin, "$(user):IDN")
{
field(DESC, "Device identification")
field(DTYP, "stream")
field(INP, "@PSU.proto idn PSU0")
field(PINI, "YES")
}
v-set-record(bo, "$(user):POWER-CM")
{
field(DESC, "Power switch command")
field(DTYP, "stream")
field(OUT, "@PSU.proto power-cm PSU0")
field(ONAM, "ON")
field(ZNAM, "OFF")
field(FLNK, "$(user):POWER-RB")
}

## Slide 8
Task: integrate a simple power supply using StreamDevice
Starting the IOC:
  Change to the directory “streamIoc/iocBoot/ioctestIoc”
    It would be good to take a look at the directory structure
  Start the IOC with the command ./st.cmd
    Pay attention to the terminal output.
  The IOC serves a number of records in addition to the PSU simulation.
    Let us look at the startup script (st.cmd) to see the commands.
In another window, type “pvget epics-dev:IDN” and check the reply.
  If you get a reply and no timeout, congratulations!
Next, let us start Phoebus. Let us work interactively from here.

## Slide 9
Success!